## Slide 1: Coverage Above and Beyond
T-Satellite

## Slide 4: LEO Satellites Used to Provide Coverage
17,500 mph
~220 miles (i)
Source: https://www.pcmag.com/news/to-improve-starlink-speeds-spacex-wants-to-orbit-satellites-closer-to-earth
Source: http://Space.com/low-earth-orbit
Source: https://docs.fcc.gov/public/attachments/DA-23-338A1.pdf
Source: https://api.starlink.com/public-files/DIRECT_TO_CELL_FIRST_TEXT_UPDATE.pdf
Source: https://www.t-mobile.com/news/network/t-mobile-starlink-beta-open-for-all-carriers
Source: https://www.t-mobile.com/coverage/satellite-phone-service
Constellation of satellites moving at 17,500 miles per hour (ii)
It takes about 90 minutes to complete an orbit of the planet. (ii)
3GPP LTE Technology
SpaceX will broadcast T-Mobile’s PCS Spectrum (Band 25). Specifically, the PCS G-block 1910-1915MHz and 1990-1995MHz will be used under a spectrum lease agreement.(iii)
First group of satellites with Direct to Cell capability launched January 2nd, 2024 and 6 days later the 1st successful txt messages were sent and received. (iv)
T-Satellite Beta Service Launch: February 9th, 2025. the first and only space‑based mobile network in the U.S. that automatically connects to your phone in areas no cellular network reaches. (v)
T-Satellite Commercial Launch: July 23rd, 2025. (vi)

## Slide 5: How can Direct to Cell Satellite Coverage help?
There are geographical areas where terrestrial wireless networks just simply are not able to cover!
National Parks do not typically allow wireless network infrastructure (power, backhaul, towers) to be built.
Mountain passes and recreational areas have historically been difficult to cover due to the terrain and heavy tree foliage.
Providing coverage to these areas would be beneficial to mobile customers and could provide life saving connectivity.
Olympic
National Park
North Cascades Hwy
Source: T-Mobile 4G/5G Coverage Map, February 2025
https://www.t-mobile.com/coverage/coverage-map
T-Mobile Coverage: Washington State
T-Mobile 4G/5G Coverage
Satellite SMS Coverage

## Slide 6: NTN is complementary (not a mobile network replacement)
The amount of spectrum allocated to NTN vs terrestrial is a major contributor when comparing system capacity.
Terrestrial Mobile Networks are able to increase capacity by adding more cells (sites) to densify the capacity of the network.
NTN networks have an advantage of providing coverage over wide areas, however the capacity per square mile is fixed.
NTN has challenges providing additional capacity if the traffic demand is localized.
NTN Fixed Coverage Grid
Mobile Network Density
Rural Areas
Urban
Dense Urban
All Areas

## Slide 7: Service Offering and Emergency Coverage Enablement
Vision to provide text message coverage, including Text to 911 and WEA practically everywhere in continental US, Hawaii, parts of Alaska, Puerto Rico and territorial waters. (i)
In Florida over the first 48 hours, the service was used to broadcast over 120 Wireless Emergency Alerts (WEA) from public safety agencies — hurricane warnings, evacuation notices, flood warnings — both in advance of Milton and when it made landfall. It has also enabled over 100K SMS messages to be sent and received. (ii)
T-Mobile’s Starlink Direct-to-Cellular was enabled in the greater Los Angeles area. During the 1st week have served approximately 198,000 users, sent/received around 96,000 SMS messages and transmitted 21 wireless alerts (WEA). (iii)
Source: https://www.t-mobile.com/news/un-carrier/t-mobile-takes-coverage-above-and-beyond-with-spacex
Source: https://www.t-mobile.com/news/network/hurricane-milton
Source: https://www.t-mobile.com/news/network/t-mobile-stands-prepared-as-wildfires-impact-southern-california
Hurricane Milton near Florida (Oct. 2024)
Wild Fires near Los Angeles (Jan. 2025)

## Slide 8: Devices with the service will continue to grow
Satellite networks work differently from traditional cellular networks, so to ensure the best possible experience, smartphones need to be satellite optimized. We’re collaborating with our handset partners to optimize as many smartphones as possible, starting with newer devices.
These devices will work with T-Mobile Starlink (this list will be updated over time in 2025) (i):
  Apple iPhone 14 and later (including Plus, Pro & Pro Max)
  Google Pixel 9 (including Pro, Pro Fold, & Pro XL)
  Motorola 2024 and later (including razr, razr+, edge and g series)
  Samsung Galaxy A14, A15, A16, A35, A53, A54
  Samsung Galaxy S21 and later (including Plus, Ultra and Fan Edition)
  Samsung Galaxy X Cover6 Pro
  Samsung Galaxy Z Flip3 and later
  Samsung Galaxy Z Fold3 and later
  REVVL 7 (including Pro)
WEA also made available to non-optimized devices regardless of carrier.
Source: https://www.t-mobile.com/coverage/satellite-phone-service
Notes: https://www.t-mobile.com/coverage/satellite-phone-service

## Slide 9: Text to 911
Text Relay
Text Control Center (TCC)
PSAP
Text to 911 Path
PSAP Routing
SCS
MNO
Voice 911 Path
  Routing to a local PSAP or Text Relay center is supported
  “Callback” number and precise location is supported
  The Text Relay center covers cases where Text to 911 service to a PSAP is unavailable
    Device location unavailable
    PSAP serving the area is not text capable
  Text Relay center confirms incident information including location and brokers communication with PSAPs as needed
“This emergency text session is over satellite. The user cannot place a voice call. Messages may be delayed.”

## Slide 10: Text to 911 Service PSAP Readiness
Current Availability
PSAP Counts
Approximately 5,100 primary PSAPs Nationwide
85% support Text to 911 service
No additional preparation required from PSAP to receive SCS Text to 911
Roaming Support
T-Mobile Text to 911 is supported regardless of home terrestrial coverage if device location is available
PSAPs must submit an RFS

## Slide 11: Thank You